Boot Process

---
Flow Diagram
- System Bios
- bootasm.S
- bootmain.c
- entry.S
- main.c
Bootloader
Kerne image

---
System Bios
- Initialization of hardware POST & also wakeup bios of other devices.
- Find boot device, pick up first sector form it puts in ram at PA 0x7c00 and starts executing in real mode with %cs=0 %ip=7c00.

---
Bootasm.s
- bootasm.S starts in 16-bit real mode and leaves in 32-bit protected mode with no hardware paging enabled
- Initial taks to land in 32 bit mode
- Call bootmain() in bootmain.c

---
Bootmain.c
- bootmain() loads an ELF kernel image from the disk starting at sector 1 and then jumps to the kernel entry routine. {i.e entry() }
- Actually reads first sector of hard disk loads the image there located at physical address 2 MB
- Control transfers to entry()